## Slide 1: IP Wireless Access in Vehicular Environments (IPWAVE) Basic Protocols Project
Champion: Jaehoon Paul Jeong
Students: Yiwen (Chris) Shen, (SKKU)
    Bien Aime Mugabarigira, (SKKU)
    Xiaohong (Dawn) Yu, (SKKU)
    Jae Won Lee, (SKKU)
    Kyoungjae Sun (SSU),
    Jinho Park (KNU)
IETF 109 Hackathon, Online
November 9-14, 2020
On-Off Mix

## Slide 2: Use Cases of Vehicular Networking
Vehicle Traffic Release
City Road Emergency
Road Intersection Passing
Navigation
Connected Automated Vehicles
Vehicle Data Forwarding Services

## Slide 3: Hackathon Plan
Implement the enhanced IPv6 ND in a Linux Kernel to enable the proposed new ND options for vehicle driving safety.
Testing the modified Linux Kernel with a robot car to verify the CNP for crash avoidance.

## Slide 4: Context-Aware Navigator Protocol over IPWAVE
Road-Context Awareness through Light-weight Message Exchange
- Cooperation Context Message (CCM) and Emergency Context Message (ECM)
CCM
ECM
Reference: “Context-Aware Navigator for Road Safety in Vehicular Cyber-Physical Systems”, The Third International Conference On Consumer Electronics (ICCE) Asia, June 2018.
http://iotlab.skku.edu/publications/international-conference/ICCE-ASIA-CAN.pdf

## Slide 5: Vehicle Mobility Information (VMI)
VMI Option as an ND Option:
Type: CCM or ECM
1
0
9
8
7
6
5
4
3
2
1
0
9
8
7
6
5
4
3
2
1
0
9
8
7
6
5
4
3
2
1
0
Type | Length | Message | Reserved 1
Reserved 2
Mobility Information
0
1
2
3

## Slide 6: Previous Work
IPv6 Packet Transmission over two OCB-enabled WiFi modules in vehicular networks
  How to enable a commercial WiFi module to work on 5.9GHz band?
  How would IPv6 ND work in IEEE OCB mode?
  How to enable webcam (dashcam) streaming by IPv6 over 802.11 OCB mode?
Context-Aware Navigation Protocol Simulation
  How can we use IPWAVE protocol for road crash avoidance?
Related IPWAVE standard Drafts:
  https://datatracker.ietf.org/doc/draft-ietf-ipwave-ipv6-over-80211ocb/
  https://datatracker.ietf.org/doc/draft-ietf-ipwave-vehicular-networking/

## Slide 7: What got done
Compiling Linux Kernel for OCB mode (Kernel version 4.4).
  Modify Makefile to remove possible errors
  Menuconfig for OCB mode
    Enable ITS G5/DSRC band
    Atheros 802.11 ath9k wireless card driver
    Enable webcam driver
IPv6 packet transmission by two OCB-enabled WiFi modules.
  IPv6 address configuration
  UDP packets transmission
  Webcam streaming
Implementation of VMI as ND Option in Linux Kernel

## Slide 8: Setup Environment

## Slide 9: Experiment
Successfully stream webcam over two OCB-enabled laptops.

## Slide 10: What We Learned
Compiling error can happen due to Makefile setting.
  Updated Makefile to remove the error
  Updated Makefile of Central Regulatory Domain Agent (CRDA) to remove a compiling flag, -Werror, that shows compiling errors when variables are not used.
  Made a new manual for running OCB mode
IPv6 ND is not automatically running on the interface.
  No Carrier shown on the interface
  Need to manually configure IPv6 address and neighbors

## Slide 11: Open Source Project at Github https://github.com/ipwave-hackathon-ietf/ipwave-hackathon-ietf-106

## Slide 13: Wrap Up
Team members:
Champions:
  Jaehoon Paul Jeong (SKKU)
Professors:
  Jaehoon Paul Jeong (SKKU)
  Yonghan Kim (SSU)
Students:
  Yiwen Chris Shen (SKKU)
  Bien Aime Mugabarigira (SKKU)
  Xiaohong (Dawn) Yu (SKKU)
  Jaewon Lee (SKKU)
  Kyoungjae Sun (SSU)
  Jinho Park (KNU)
Video clip demo: https://youtu.be/gQxOLU740b4
https://www.youtube.com/watch?v=6Ss5OzV88so
Where to get code (manual):
https://github.com/ipwave-hackathon-ietf/ipwave-hackathon-ietf-106
Original contributors:
Czech Technical University and Volkswagen:
https://ctu-iig.github.io/802.11p-linux/